Name	Size	Begin Address	End Address	Description
Main program memory	8 kw	0x0000	0x1FFF	Main program memory. Port A connected to general purpose, Port B is connected to program counter.
Sprite Object Data	1 kw	0x2000	0x23FF	Sprite object data. 256 objects, each 4 words.
Sprite Tile Data	8 kw	0x2400	0x43FF	Sprite table VRAM, organized by tile, into two tables.
Palette Data	1 kw	0x4400	0x47FF	Palette storage.
GPU status register	1 w	0x4800		Status flags for GPU / [0] vbright / [1] hbright
Sprite Priority	1 byte	0x4801		Which sprite will be drawn first.
Screen Brightness	1 byte	0x4802		Screen brightness (fade). 0 is all off, 255 is all on.
Switches	1 byte	0x4803		[3:0] is the toggle switches / [4] is East pushbutton / [5] is North pushbutton / [6] is West pushbutton / [7] is rotary shaft pushbutton
DMA Src Lower	1 word	0x4804		Direct memory access for copying large chunks of data from flash ROM to RAM. Lower 16 bits of ROM src address.
DMA Src Upper	1 word	0x4805		Upper 7 bits of ROM src address.
DMA Dst	1 word	0x4806		RAM dst address.
DMA Amount	1 word	0x4807		On write of Amount, processor is stalled until Amount words have been copied from ROM to RAM.
Rotary Encoder	1 word	0x4808		16-bit signed number, where positive is a right, negative is left. Writing to the register sets the counter to given value.
Random Number Generator	1 word	0x4809		Reading from the RNG generates a new random number. Writing to the RNG writes a seed value.
Controller A	1 word	0x480a		Game controller A register. / [11] left / [10] right / [9] up / [8] down / [7] A / [6] B	[5] X / [4] Y / [3] L / [2] R / [1] select / [0] start
Controller B	1 word	0x480b		Game controller B register.
Sounds				Sound data stored in flash.
b_rom_addr [15:0]		0x480c
b_rom_addr [23:16]		0x480d
bamp		0x480e
b_duration [15:0]		0x480f
b_duration [31:16]		0x4810
s0_rom_addr [15:0]		0x4811
s0_rom_addr [23:16]		0x4812
sfx_amp0 [3:0]		0x4813
s0_duration [15:0]		0x4814
s0_duration [31:16]		0x4815
s1_rom_addr [15:0]		0x4816
s1_rom_addr [23:16]		0x4817
sfx_amp1 [3:0]		0x4818
s1_duration [15:0]		0x4819
s1_duration [31:16]		0x481a
s2_rom_addr [15:0]		0x481b
s2_rom_addr [23:16]		0x481c
sfx_amp2 [3:0]		0x481d
s2_duration [15:0]		0x481e
s2_duration [31:16]		0x481f
s3_rom_addr [15:0]		0x4820
s3_rom_addr [23:16]		0x4821
sfx_amp3 [3:0]		0x4822
s3_duration [15:0]		0x4823
s3_duration [31:16]		0x4824
SOUND_TOP_ADDR = 16'h4825,		0x4825
Blank signal		0x4826		1 bit blank_time_up signal
bg_palette	1 word	0x4827		Used to change palette