Name	Size	Begin Address	End Address	Description
Main program memory	8 kw	0x0000	0x1FFF	Main program memory. Port A connected to general purpose, Port B is connected to program counter.
Sprite Object Data	1 kw	0x2000	0x23FF	Sprite object data. 256 objects, each 4 words.
Sprite Tile Data	8 kw	0x2400	0x43FF	Sprite table VRAM, organized by tile, into two tables.
Palette Data	1 kw	0x4400	0x47FF	Palette storage.
GPU status register	1 w	0x4800		Status flags for GPU (Includes vbright and hbright)
Sprite Priority	1 byte	0x4801		Which sprite will be drawn first.
Screen Brightness	1 byte	0x4802		Screen brightness (fade). 0 is all off, 255 is all on.
Controller A	1 word	0x4803		Game controller A register.
Controller B	1 word	0x4804		Game controller B register.
Random Number Generator	1 word	0x4805		A Linear Feedback Shift Registers feed each of the bits.
Counter Upper	1 word	0x4806		MSB of 32 bit counter. Should read MSB first for more accurate LSB reading. (about 85.9 second period)
Counter Lower	1 word	0x4807		LSB of 32 bit counter. Increments every clock cycle. Writing sets the counter to the written value.
DMA	4 words	0x4808	0x480B	Direct memory access for copying large chunks of data from flash ROM to RAM. (lowest priority). (SrcMSB, SrcLSB, Target, Amount.) On write of amount, processor is stalled until Amount words have been copied from Src to Target.