Name	Size	Begin Address	End Address	Description
Main program memory	9 kw	0x0000	0x23FF	Main program memory. Port A connected to general purpose, Port B is connected to program counter.
Sprite Object Data	1 kw			Sprite object data. 256 objects, each 4 words.
Sprite Tile Data	8 kw			Sprite table VRAM, organized by tile, into two tables.
Palette Data	1 kw			Palette storage.
GPU status register	1 w			Status flags for GPU (Includes vbright and hbright)
Sprite Priority	1 byte			Which sprite will be drawn first.
Screen Brightness	1 byte			Screen brightness (fade). 0 is all off, 255 is all on.
Controller A	1 word			Game controller A register.
Controller B	1 word			Game controller B register.
Random Number Generator	1 word			A Linear Feedback Shift Registers feed each of the bits.
Counter Upper	1 word			MSB of 32 bit counter. Should read MSB first for more accurate LSB reading. (about 85.9 second period)
Counter Lower	1 word			LSB of 32 bit counter. Increments every clock cycle. Writing sets the counter to the written value.
DMA	4 words			Direct memory access for copying large chunks of data from flash ROM to RAM. (lowest priority). (SrcMSB, SrcLSB, Target, Amount.) On write of amount, processor is stalled until Amount words have been copied from Src to Target.