Address	Name	Description	Read	Write
0x0000	null	Null
0x0001-0x1FFF		8 kword main program memory
0x2000-0x3FFF		8 kword sprite table VRAM
0x4000-0x41FF	sprite[i][j]	Sprite object data. 128 objects, each 4 words.	See sprite data document for details.
0x4200-0x437F	palette	Palette storage.	See palette documentation.
0x4382	gpuctr	GPU control register	abcdefghijklmnop / g is hbright / h is vbright	Upper 8 bits are read only.
0x4380	spritePriority	Which sprite will be drawn first.
0x4381	brightness	Screen brightness (fade). 0 is all off, 255 is all on.
[0x4382-0xFFF7]	Rom	Any remaining memory used for ROM. Read only memory from external flash.	Takes 75 ns (4 clocks) to read from external flash.	ignored
0xFFF8	dmaSrc	16 bit memory address of initial block to copy from.	Direct memory address is a way to copy large blocks of data, bypassing the standard data path.
0xFFF9	dmaDst	16 bit memory address of intitial block to copy to.
0xFFFA	dmaCount	Number of words to be copied.		On write, suspends processor until dmaCount words have been copied from dmaSrc to dmaDst
0xFFFB	counterMSB	32 bit counter, incremented every clock cycle. (about 85.9 second period)	Read counter upper 16 bits. Should read MSB first for more accurate LSB reading.	Set counter upper bits.
0xFFFC	counterLSB	Lower 16 bits of counter.	Read counter lower 16 bits.	Set counter lower bits.
0xFFFD	contra	Controller A	Read the value of the controller A register.	ignored
0xFFFE	contrb	Controller B	Read controller B.	ignored
0xFFFF	rng	Random number generator.	Read the next random number.	Write the seed value.