ADDR + 0
Field	Size	Description
X	[15:0]	Current signed integer X-coordinate of the sprite

ADDR + 1
Field	Size	Description
Sprite Y	[3:0]	Sprite table Y (index of upper left tile)
Sprite X	[3:0]	Sprite table X (index of upper left tile)
Sprite Table		Which of the two 16x16 sprite tables to use.
PaletteId	[3:0]	ID number of the palette this sprite will use.
Unused	[2:0]	Unused space, available for more features.

ADDR + 2
Field	Size	Description
Y	[15:0]	Current signed integer Y-coordinate of the sprite

ADDR + 3
Field	Size	Description
Active		True if sprite should be drawn.
Z	[1:0]	Z-layer of the sprite. A sprite with a higher Z will be on top of a sprite with a lower Z.
VFlip		Vertically flipped if true.
HFlip		Horizontally flipped if true.
SizeY	[2:0]	Vertical size of the sprite. Same format as SizeX.
SizeX	[2:0]	Horizontal size of the sprite. / Value 0 1 2 3 4 5 6 7 / Pixels 8 16 24 32 40 48 56 64
Unused	[4:0]	Unused space, available for more features.

Sprite data consists of 4 16-bit words, or 64 bits.

Currently, there are 256 sprites, comprising a 1024 word block ram.